## Slide 2
101 Workshop
3D Printing -
Keepsakes and Talismans

## Slide 3
Acknowledgement of country
We acknowledge Aboriginal and Torres Strait Islander peoples and their continuing connection to land and as custodians of stories for millennia. We respectfully acknowledge the land on which we all meet today, and pay our respects to elders past, present and emerging.

## Slide 4
Health & Safety
Exit points
Lab Risk Assessments
Safe operating procedures

## Slide 5
Today we will:
Introduce you to the concept of Talismans and Keepsakes in the context of Dearly Departed.
Introduce you to Tinkercad.
Guide you through a process of design and support you to personalise a talisman/keepsake.
You will leave with a talisman inspired by the Dearly Departed exhibition.
Workshop Overview

## Slide 6: What you’ll create
In this workshop we will guide you through the process of preparing a 3D keepsake for printing that you will learn how to personalise using Tinkercad
After attending this session, you should have a better understanding of the various issues that influence printing success, print speed, strength, and surface quality.

## Slide 7
This workshop will reference objects and concepts associated with death and dying.
These can evoke emotions, memories, or personal reflections. You are encouraged to take breaks whenever needed in the workshop, should you need to take some time for yourself.
The QR code to the right contains information about services that offer free and confidential non-urgent support.
Social and emotional wellbeing
https://www.slq.qld.gov.au/support

## Slide 8
A keepsake is a small memento or token meant to symbolise a memory of a significant person, place or event.
What are keepsakes and talismans?
We value keepsakes because they prompt nostalgic memories of the past. But perhaps more importantly, we also value them because they afford a feeling of contact with that which they remind us of.
An excerpt from the Handbook of Nostalgia.
Windsor 2024: Routledge
A Talisman is an object, typically an inscribed ring or stone, that is thought to have magic powers or bring good luck.

## Slide 9
Death is a universal experience. It will come to us all. Yet the way we confront, discuss, experience and ultimately reckon with death, and the realities of dying, varies enormously. Culturally diverse traditions and practices around death offer unique insights into how communities around the world honour and mourn their loved ones, shaping vastly different experiences and understandings of life’s final chapter.
Throughout the 20th century, death became a quiet taboo; something rarely spoken of, despite touching every life. Positioned at the powerful intersection of history, art and emotion, Dearly Departed encourages audiences to reflect on what it means to live well, die well and honour those who came before us. It reframes death not as an ending, but as a profound and enduring part of Queensland’s living story.
Innovative, accessible, and deeply human, Dearly Departed: death in life invites visitors into a bold exploration of mortality across Queensland’s past, present and future. Through rich historical insight, evocative artistic interpretation and interactive design, the exhibition sparks meaningful conversation about life, death and the memories we hold.
DEARLY DEPARTED

## Slide 11
Keepsakes in Dearly Departed

## Slide 12
My own collection

## Slide 13
Your own collection
Take a moment to think about a keepsake or a talisman that you have in your collection of items.
Is there something that you have that symbolises a memory of a significant person, place or event?

## Slide 14
Okay!
Let’s learn more about 3D printing

## Slide 15: OPEN LAB
Open Lab sessions are a chance to meet up with like-minded makers and tinkerers at The Edge. Facilitators are available to support your creative needs in the space. You can attend Hack the Evening on Thursdays from 5pm – 8pm to print your 3D designs with staff support (pending printer availability).
Wednesday 12pm – 5pm
Thursday 1.30pm – 8pm
Saturday 12pm – 5pm
For more info and to book, head to https://www.slq.qld.gov.au/visit/spaces/edge

## Slide 16
What is a 3D Model?
A 3D model is a digital construction of an object or design in three dimensions. Creating (or otherwise obtaining) a 3D model is essential for 3D printing. 3D models are exchanged as digital files, of which there are many file types. When preparing printing, we primarily focus on STL files.

## Slide 17
What is 3D Printing?
3D printing is the construction of a physical 3D object from a digital 3D model. The process typically involves material (plastics, metals, wax, ceramics, concrete) being deposited, joined and solidified layer-by-layer under computer control.

## Slide 18
Prusa i3 MK3S+ FFF/FDM Printer
A motorised, computer-controlled device which converts a digital 3D model into a physical 3D object by following a list of sequential instructions (G-code) compiled by specialised slicing software (PrusaSlicer). Plastic filament is fed into a moving print head, remelted, then precision-deposited layer upon layer onto a movable bed.

## Slide 19
Your answers to the following questions will help guide your process:
How are you going to use the print? Is it a functional or purely decorative object?
How much post-print finishing and assembly do you want to do?
Decisions you make around settings in the slicing software will impact whether the printed object meets your expectations regarding strength and appearance.
What do you expect of the printed object?

## Slide 20
What is Slicing?
The act of converting a 3D model into a set of instructions a 3D printer can execute is called Slicing. Slicing is a critical step in the process of 3D printing.
Below are the primary factors that require decisions when preparing a 3D model for printing using PrusaSlicer:
Print Settings (thickness of each layer; quality versus speed)
Filament (choice on Open Lab computers limited to filament brands/polymers on hand)
Printer (choice on Open Lab computers limited to 2 printer models and 0.4mm nozzles)
Supports (removable scaffold printed where necessary to provide support for object geometry [overhangs, undercuts] that would otherwise not print successfully. Which support type? Where are they required?
Infill (the geometry and density of the internal structure to be between the external walls of the object.
3D Model
(typically an STL file)
Slicing
(G-code file)
3D Printer

## Slide 21
Slicing Decisions
Speed will always compromise quality
Quality is clear option for overnight print runs
Infill > than 30% will not improve strength
Assign supports ‘Everywhere’ for unattended print runs
Can less filament be used or surface quality improved by reorienting a model on the plate?
Can less filament be used or surface quality improved by cutting the model into sections?

## Slide 22
Places to download include:
Printables (also accessible through a menu tab appearing at the top of the PrusaSlicer window
Thingiverse
Tinkercad library
Many other free and fee sites
Sourcing Existing Models

## Slide 23
Let’s get designing

## Slide 24
TinkerCAD
Pros​
Free​
Great intuitive software for getting started​
Browser based​
​
Cons​
Experienced designers might get frustrated with the lack of features​
But it’s perfect for what we are doing today, and you should walk away feeling confident to continue to experiment.

## Slide 27: Let’s have a look at the tools

## Slide 28: Navigating the 3-dimensional space
Moving around
  Zoom in and out using the scroll wheel
Pan & Tilt
  Right click and drag to change the aspect of your view or
  Click and drag the Cube device to rotate you view angle
  If you get lost click the home icon and it will take you back to the default view

## Slide 29
Navigating the 3-dimensional space
Moving around ​
Zoom in and out using the scroll wheel​
​
Pan & Tilt​
Right click and drag to change the aspect of your view or​
Click and drag the Cube device to rotate you view angle​
If you get lost click the home icon and it will take you back to the default view​
​

## Slide 30
Moving and manipulating shapes
Select
Using the left click (hold shift select multiple objects)
Or left click and drag a selection box around multiple objects
Resizing
Left click and drag the black or white handles to resize your shapes
Hold the SHIFT key to constrain proportions
Left click and drag the black arrow to change the elevation of the shape in relation to the work plane
Moving
You can nudge a selected object around the x & y axes with the arrow keys
Rotate
Left click and drag the arched arrows (3 of them for X, Y, Z) to rotate an object, you can also type in an angle once it is highlighted.
Ruler
Drag the ruler out onto the workplace to resize or arrange shapes using typed in dimensions

## Slide 31: Moving and manipulating shapes
Resizing
  left click and drag the black or white handles to resize the your shapes.
  Hold the SHIFT key to constrain proportions.
  Left click and drag the black cone to change the elevation of your in relation to the work plane

## Slide 32: Moving and manipulating shapes
Moving
You can nudge a selected object around the x & y axes with the arrow keys
Rotate
Left click and drag the curly one of the 3 arrows to rotate an object. Once the angle highlighted you an type in an angle too.*
*it can be difficult to realign an object’s angle once you’ve moved it so be deliberate with these changes

## Slide 33: Moving and manipulating shapes
Ruler
  Drag the ruler out onto the workplane to resize or arrange shapes using typed in dimensions.

## Slide 34: Make a complex shape
Grouping solids and holes
You can make complex shapes by combining and subtracting the primitive (basic) shapes using the group tool.
Select the objects you want to combine
And then hit the group button

## Slide 35: Make a complex shape
Grouping solids and holes
You can make complex shapes by combining and subtracting the primitive (basic) shapes using the group tool.
Select the objects you want to combine
And then hit the group button

## Slide 36
Let’s get in there
We are going to create a simple amulet to learn these tools

## Slide 37
Setting up the shape

## Slide 38
Setting up the shape

## Slide 39
Put that shape to the side for later

## Slide 40
Setting up the shape
Going to create two more shapes
Shape 1
Same dimensions as before 35mm x 26mm
Shape 2
Slightly smaller (we are removing 3mm from both width and height
32mm x 23mm

## Slide 41
Aligning the shape
Select the shapes you want to align
Click the align tool (circled top right)
Click the black circles as needed to orientate it

## Slide 42
Creating a hole in the shape

## Slide 43
Now we will combine the shape

## Slide 44
And set the height of the shape

## Slide 45
Printables

## Slide 46
Details smaller than the printer nozzle diameter (0.4mm) will not print successfully. Problem details can possibly be separated as parts and deleted (depending on the model) or cut and discarded.
Will you be able to remove printed support scaffolding from areas where it is required? Will the model need to be cut into parts for post-print assembly to facilitate supports removal?
Does the model have missing surfaces or open edges that require repair?
Models should be oriented on the plate to achieve the best balance of strength, surface quality, and minimal supports. If cutting your model, the cut faces should be placed on the build plate.
Some additional reading - https://www.ugent.be/ea/architectuur/nl/info-voor-studenten/atelier-faciliteiten/preparing-files-for-3d-printing-file-fixing-terminology-explanation-and-checklist
What to consider when sourcing a 3D model

## Slide 47
Exporting
Hit the export button and select STL
Save to your desired folder
Open file up in PrusaSlicer using one of our facility computers. The software will be configured correctly on our computers.

## Slide 48: Key notes for giving us your files
Please do the following on the USBs
Make a folder with your first and last name
Save your G-code file AND your project file in there
Let me know if you want a particular colour filament (blue, yellow, black, white) and loop or no loop on your locket box

## Slide 49: OPEN LAB
Open Lab sessions are a chance to meet up with like-minded makers and tinkerers at The Edge. Facilitators are available to support your creative needs in the space. Bookings are required to use the equipment. You will be able to book equipment with your SLQ account once you have completed the relevant induction/s. Open Lab hours:
Wednesday 12pm – 5pm
Thursday 1.30pm – 8pm
Saturday 12pm – 5pm
For more info and to book, head to https://www.slq.qld.gov.au/visit/spaces/edge

## Slide 50
THANKS FOR ATTENDING
Please complete our survey that will be sent out via Eventbrite.
Tag us on socials@statelibraryqld
Contact us on appliedcreativity@slq.qld.gov.au